## Slide 1: Modeling of Electromagnetic Wave Propagation in NIM using FDTD Technique
Supervisor:
Attique Dawood
Group Member:
Muhammad Junaid Nasir (10-0361)

## Slide 2: Introduction & motivation
Invisibility cloaking
Northrop Grumman B-2 Spirit
Image courtesy:
http://www.conservativerefocus.com/blog5.php/2012/01/05/scientists-say-event-cloaking-now-possible-materials-designed-to-adjust-speed-of-light-could-obscure-events
http://www.airforce-technology.com/projects/b2/
http://spectrum.ieee.org/semiconductors/metamaterials/
Notes: Many earlier cloaking systems turned objects "invisible" only under wavelengths of light that the human eye can't see
40,000 lb (18 Tons) 150 tons total weight
1997. Undetectable in radar
Radar-absorbent material (RAM)

## Slide 3: Negative Index Materials (NIM)
Negative Index Materials (NIM) or Left Handed Material (LHM) is a material which has negative permeability and permittivity.
  When a light enters from one medium to another with different refractive indices, it alters its path depending upon the difference between the refractive indices. (Refraction)
Engineered materials
  Split-ring resonator array
  Nanotransfer Printing
Image courtesy:
1) http://randommization.com/2011/08/19/making-light-bend-the-wrong-way-with-science/
2) UC Berkeley
3) NASA Glenn Research Center

## Slide 4: Project Objectives
To simulate and observe the behavior of Electromagnetic Waves when they pass through negative index materials
To use FDTD algorithm and modify it for negative index material simulations
Reducing computational time by using the parallel processing power of Graphics Processing Units (GPU)
Comparison of algorithm performance on different platforms (MATLAB, C++, GPU)

## Slide 5: Problem Statement
model an NIM (slab) using (frequency dependent dispersive) drude model that will effectively have refractive index of -1 (choosing µr and єr = -1) at 3 GHz

## Slide 6: Deliverables
S. No | Task | Status
1 | Learning FDTD technique | Complete
2 | Implementation of FDTD algorithm in MATLAB | Complete
3 | Frequency domain analysis of medium | Complete
S. No | Task | Status
1 | Modeling of NIM | Complete
2 | Code conversion in C++ | Complete
3 | GPU programming | Complete
4 | Performance analysis | Complete

## Slide 7: FDTD
Finite-Difference Time-Domain (FDTD) is one of the most efficient techniques of differential time domain numerical modeling methods
  It solves the Maxwell’s differential equations in leap-frog manner (At a given time instant, first electric field and then magnetic field is solved)
  It is readily parallelizable on hardware like GPU

## Slide 8: FDTD
Notes: Update equations
Recursive

## Slide 9: Results
Stable Simulation with correct output
Sources
  Guassian
  3GHz Sine

## Slide 10: Limitations of FDTD Algorithm
Cannot cater for negative values of permittivity or permeability (unstable results)
This is because of the Courant stability criterion
Solution: Drudes Model

## Slide 11: Drude Dispersive Model
It relates the net force on charges moving under the influence of an electric field and facing an impeding force due to collisions with material
Not only depends on pervious spatial value of a parameter but also on pervious time-step value
2 main update equations for By & Dz, 2 auxiliary equations for Hy & Ez

## Slide 12: Flow graph of algorithm
Initialize simulation parameters
Allocate data arrays
Initialize simulation parameter arrays
Compute By & Hy
Compute Dz & Ez
Update source node
T= maxTime ?
Compute transmission & reflection coefficient
Compute refractive index of slab
No
Yes
Initialization
Post-Processing
Simulation

## Slide 13: Results
A slab of left handed material is placed in free space
A sine wave of 3 Ghz is passed through it

## Slide 14: Observations
Sinusoidal wave
  Phase velocity is negative
  Group velocity is still positive
Gaussian pulse
  Different velocities for different frequencies
Notes: The phase velocity of a wave is the rate at which the phase of the wave propagates in space.
The group velocity of a wave is the velocity with which the overall shape of the waves' amplitudes — envelope of the wave — propagates through space
Gaussian pulse since there are a number of frequency components present, they will be split up in time-domain owing to different velocities for different frequencies in the slab
A material is dispersive if its permittivity or permeability is dependent on frequency

## Slide 15: Results
Calculated Refractive Index
Simulation Results

## Slide 16: Problems
Grid truncation
Boundary condition

## Slide 17: Code conversion in C++
Problems:
File handling
Solution:
Change development environment to Linux
Chart: Performance Comparison
| 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
C++ (win 1) | 1.3491 | 1.8951 | 3.0512 | 5.1683 | 6.5504 | 13.5978 | 25.7075 | 87.941 | 180.439 | 327.479 | 534.474
C++ (Linux 1) | 0.12597 | 0.22637 | 0.91653 | 3.0965 | 7.5691 | 11.933 | 26.1995 | 52.8916 | 106.198 | 232.041 | 379.317
C++ (linux) | 0.03946 | 0.068043 | 0.13436 | 0.26363 | 0.50696 | 1.0149 | 2.09 | 4.2423 | 8.4781 | 17.0343 | 33.9552
C++ (win) | 0.13201 | 0.24501 | 0.48403 | 1.0751 | 1.9731 | 4.6593 | 7.2584 | 16.813 | 32.5549 | 60.5085 | 101.469

## Slide 18: GPU Programming
AMD Radeon HD 6770M
  Fast middle class graphics card
  256 cores
  1GB memory
  625 Mhz
  716 Million transistors
  128 bit memory bus width
  Does not support Double data type
Source: http://www.notebookcheck.net/AMD-Radeon-HD-6770M.43955.0.html
Notes: Double 64 bit with 15 digit precession
Float is 32 bit with 7 digit precession

## Slide 19: GPU Programming
OpenCL (Open Computing Language)
  Open source
  Framework for writing programs that execute across heterogeneous platforms (CPUs, GPUs, FPGAs, DSPs)
  Provides parallel computing using task-based and data-based parallelism
  Give an application access to a graphics processing unit for non-graphical computing
Source: https://www.khronos.org/opencl/

## Slide 20: Problems
Read Delay
Kernel Synchronization
Solutions:
  Increased snapshot intervals
  Boundary conditions also moved into kernel
  Balancing the work load between kernels

## Slide 21: Performance Analysis
Chart: Performance Comparison
| 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576 | 2097152 | 4194304 | 8388608 | 16777216
Matlab | 0.59134 | 0.99971 | 1.7086 | 3.3255 | 4.9397 | 8.0053 | 18.1606 | 38.6736 | 79.6862 | 161.6021 | 325.6458 | 653.1407 | 1322.5068 | 2653.2643 | 5586.3582
C++ (linux) | 0.03946 | 0.068043 | 0.13436 | 0.26363 | 0.50696 | 1.0149 | 2.09 | 4.2423 | 8.4781 | 17.0343 | 33.9552 | 68.6298 | 137.746 | 275.383 | 575.762
OpenCL (CPU) | 1.1341 | 0.86843 | 1.2092 | 1.8743 | 3.1197 | 5.8562 | 11.5163 | 23.9191 | 45.6766 | 91.5058 | 183.49 | 362.211 | 740.911 | 1523.82 | 3116.27
OpenCL (GPU) | 1.2707 | 1.1143 | 1.2952 | 1.2845 | 1.9202 | 2.2463 | 3.2987 | 5.1194 | 7.8305 | 12.8775 | 22.6828 | 48.2751 | 83.7389 | 176.589 | 328.016
C++ (win) | 0.13201 | 0.24501 | 0.48403 | 1.0751 | 1.9731 | 4.6593 | 7.2584 | 16.813 | 32.5549 | 60.5085 | 101.469 | 266.489 | 489.697 | 650.421 | 880.659
Notes: 2^24 max

## Slide 22: Performance Analysis
Chart: Performance Comparison
| 1024 | 2048 | 4096 | 8192 | 16384 | 32768
Matlab | 0.59134 | 0.99971 | 1.7086 | 3.3255 | 4.9397 | 8.0053
C++ (linux) | 0.03946 | 0.068043 | 0.13436 | 0.26363 | 0.50696 | 1.0149
OpenCL (CPU) | 1.1341 | 0.86843 | 1.2092 | 1.8743 | 3.1197 | 5.8562
OpenCL (GPU) | 1.2707 | 1.1143 | 1.2952 | 1.2845 | 1.9202 | 2.2463
C++ (win) | 0.13201 | 0.24501 | 0.48403 | 1.0751 | 1.9731 | 4.6593
Notes: 2^15 max
2^14 c++ win better then gpu

## Slide 23: Performance Analysis
Chart: Performance Comparison
| 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288
C++ (linux) | 0.03946 | 0.068043 | 0.13436 | 0.26363 | 0.50696 | 1.0149 | 2.09 | 4.2423 | 8.4781 | 17.0343
OpenCL (GPU) | 1.2707 | 1.1143 | 1.2952 | 1.2845 | 1.9202 | 2.2463 | 3.2987 | 5.1194 | 7.8305 | 12.8775
C++ (win) | 0.13201 | 0.24501 | 0.48403 | 1.0751 | 1.9731 | 4.6593 | 7.2584 | 16.813 | 32.5549 | 60.5085
Notes: 2^15 max
2^18 c++ better then gpu

## Slide 24: Performance Analysis
Chart: Performance Comparison
| 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576 | 2097152 | 4194304 | 8388608 | 16777216
Matlab | 0.59134 | 0.99971 | 1.7086 | 3.3255 | 4.9397 | 8.0053 | 18.1606 | 38.6736 | 79.6862 | 161.6021 | 325.6458 | 653.1407 | 1322.5068 | 2653.2643 | 5586.3582
C++ (linux) | 0.03946 | 0.068043 | 0.13436 | 0.26363 | 0.50696 | 1.0149 | 2.09 | 4.2423 | 8.4781 | 17.0343 | 33.9552 | 68.6298 | 137.746 | 275.383 | 575.762
OpenCL (CPU) | 1.1341 | 0.86843 | 1.2092 | 1.8743 | 3.1197 | 5.8562 | 11.5163 | 23.9191 | 45.6766 | 91.5058 | 183.49 | 362.211 | 740.911 | 1523.82 | 3116.27
OpenCL (GPU) | 1.2707 | 1.1143 | 1.2952 | 1.2845 | 1.9202 | 2.2463 | 3.2987 | 5.1194 | 7.8305 | 12.8775 | 22.6828 | 48.2751 | 83.7389 | 176.589 | 328.016
C++ (win) | 0.13201 | 0.24501 | 0.48403 | 1.0751 | 1.9731 | 4.6593 | 7.2584 | 16.813 | 32.5549 | 60.5085 | 101.469 | 266.489 | 489.697 | 650.421 | 880.659

## Slide 25: Platform Comparison
For big simulation size GPU is faster
  Than MATLAB by the factor of 20 (times)
  Than C++ (Windows) by the factor of 3 (times)
  Than C++ (Linux) by the factor of 2 (times)
For simulation size of 2^14 or less c++ is a better option than GPU

## Slide 26: References
[1] S. G. et al, “Metamaterials and fdtd based numerical modeling studies," ELECO, Sep 2007.
[2] J. B. Schneider, Understanding the Finite Dierence Time-Domain Method. www.eecs.wsu.edu/~schneidj/ufdtd, 2010.
[3] Y. H. Argyropoulos C., Yan Zhao, “A radially-dependent dispersive finite-dierence time-domain method for the evaluation of electromagnetic cloaks," IEEE Transactions on Antennas and Propagation, vol. 57, pp. 1432{1441, May 2009.
[4] R. W. Ziolkowski and E. Heyman, “Wave propagation in media having negative permittivity and permeability," Physical Review, vol. 64, October 2001.
[5] Ryoji Tsuchiyama, Takashi Nakamura, Takuro Iizuka, Akihiro Asahara, Jeongdo Son, Satoshi Miki, The OpenCL Programming Book, 1st ed. , Fixstars, March 2010.

## Slide 27: Thank You

## Slide 28: Phase & Group velocity
The phase velocity of a wave is the rate at which the
phase of the wave propagates in space. any given phase of the wave (for example, the crest) will appear to travel at the phase velocity
The group velocity of a wave is the velocity with which the overall shape of the waves' amplitudes — known as the modulation or envelope of the wave — propagates through space
Credits: Kraaiennest, Geek3