## Slide 1: Modeling of Electromagnetic Wave Propagation in NIM using FDTD Technique
Supervisor:
Attique Dawood
Group Member:
Muhammad Junaid Nasir (10-0361)

## Slide 2: Project Objectives
To simulate and observe the behavior of Electromagnetic Waves specifically phenomenon of refraction when they pass through negative index materials
To use FDTD algorithm and modify it for negative index material simulations
Comparison of algorithm performance on different platforms

## Slide 3: Introduction to NIM
Negative Index Materials (NIM) or Left Handed Material (LHM) is a material which has negative permeability and permittivity.
  when a light enters from one medium to another with different refractive indices, it alters its path depending upon the difference between the refractive indices. (Refraction)
  Naturally value of refractive index is always positive

## Slide 5: Deliverables
FYP 1
  Learning FDTD technique
  Implementation of FDTD algorithm in Matlab
  Frequency domain analysis of medium
FYP 2
  Analysis of EM wave in NIM
  GPU implementation
  Application Specific analysis (Super lense)
  Performance Analysis

## Slide 6: Task 1: FDTD Technique
Why FDTD ?
Problems

## Slide 7: How FDTD works
Write Ampere's and Faraday's laws in the form of finite differences. Writing them in the form of electric and magnetic field as the derivative of time and space.
Solve equation so that we can get future values from past values
Notes: change in the E-field in time (the time derivative) is dependent on the change in the H-field across space (the curl)
ε permittivity (extent to which it concentrates electrostatic lines of flux. In technical terms, it is the ratio of the amount of electrical energy stored in a material by an applied voltage, relative to that stored in a vacuum )
µ permeability ( the ability of a material to support the formation of a magnetic field within itself. In other words, it is the degree of magnetization that a material obtains in response to an applied magnetic field.)

## Slide 8: How FDTD works
We can find magnetic field using past values of electric field also find electric field values using past magnetic field values.
Repeat the above step to get all values

## Slide 9: How FDTD works

## Slide 10: Task 2: Implementation On MATlab
Both sinusoidal and Gaussian waves
F = 3 Ghz

## Slide 11: Task 3: Frequency Domain Analysis
Medium under observation is shown
ε permittivity = 2 εo

## Slide 12: Additional Task: Implementation in C++
Problems
  File handling
  Data Types

## Slide 13: Questions ?

## Slide 14: Applications of NIM
Super lense
Notes: is a lens which uses metamaterials to go beyond the diffraction limit